Scientific Experimentation and Evaluation
Hochschule Bonn-Rhein-Sieg

Team members:
- Carlo Wiesse
- Mihir Mulye

HW Description:
(1) On the last three lecture slides, you will find the description of a soft tissue measurement experiment. Apply the appropriate terms from the slide "2B: Formalization general terms" to this description.
(2) Complete assignment 1.1 from the manual and upload deliverable 1.1.
Again use the appropriate terms to describe your setup.

Problem #1
Measurand: Axial force and indentation depth.

Measurement:
Newton (N): Unit used to express axial force.
Millimeter (mm): Unit used to express indentation depth.

Display: Not provided.

(Display) Range: Not provided.

Measurement range: Not provided.

Suppression area: The indentation depth was decided to be chosen between 0 - 11.5 mm.

Measured (Quantity) Value : Both axes in a plot. For example, in the following plot, the “measured force” variable is getting values assigned to it on the y-axis. Similarly, the “time” variable is getting values assigned to it on the x-axis.

Measurement result:
For example:
Maximum peak to peak value over this test is 0.0987 N. Standard Deviation of the noise is 0.0042 N.

Device Under Test (DUT): Simulab complex tissue model.

Measurement facility:
The measurement facility is composed by:
PI hexapod
Monocarrier drive
Indentation tool
Simulab complex tissue model
ATI Mini40 force sensor
EPOS2 motor controller

Measurement System:
The measurement system is composed by:
EPOS2 motor controller
Indentation tool
FT sensor
NI DAQ

Meter:
The meter is composed by:
FT sensor
NI DAQ

Measuring Principle: Deformation due to induced external loading.

Measuring method:
1. Displace the material using the indentation tool.
2. Measure the applied force using FT sensor.
3. Consider the Simulab complex tissue model and read its response.

Sensitivity: Not provided.

References
[1] The images included in the solutions are included from the lecture slides titled ‘Measurement as a process’.

Report for Scientific Experimentation and Evaluation

Aim
To construct a LEGO Differential Drive Robot and measure the observable end pose variation for three different paths followed by the robot namely arc to left, arc to right and go straight. Repeat the experiment 20 times.

Design of the Robot
The robot is a differential drive assembly with a castor wheel mounted at the back. Two differentially driven wheels are mounted on the front axle. Camera is mounted on top of the robot to increase the field of vision to aid with ‘Aruco’ approach.

Approaches

Standard Approach
Step 1: Place the robot in a specified initial position and then check the position (using marker).
Step 2: Run the program and verify whether the robot exhibits the desired behaviour.
Step 3: Let the execution complete and measure the final position using conventional methods (ruler/measuring tape).
Step 4: Record results and calculate errors.

Aruco Approach
Step 1: Place the robot in a specified initial position and then check the position using the camera (using ‘Aruco’ library).
Step 2: Run the program and verify whether the robot exhibits the desired behaviour.
Step 3: Let the execution complete and measure the final position using camera (using ‘Aruco’ library).
Step 4: Record results and calculate errors.

Problem Description

Problem faced
- Replicating initial position over the iterations might be tedious.
- Measuring the final pose of the robot might be difficult to accomplish.
- The robot might overshoot the final position and the camera might not be able to locate the QR pattern.

Sources of Error
- ‘Slippage’ may take place between the wheels and surface and introduce some error in the final desired location of the robot.
- Errors in actuation of motors while turning.

Possible Solutions
- Demarcating the initial position of the robot by plotting the top view of the wheel on the sheet.
- Create a contraption from the LEGO pipes to superimpose on a mark already drawn on the sheet.
- Making use of Quick Response markers with ‘Aruco’ package (OpenCV) to eliminate the errors introduced due to variations in initial position.
- Using a pen/ruler to mark the initial position of the robot.

References
[1] https://github.com/mhwasil/camera_calibration